## Slide 1: Privacy-Preserving Multicast to Explicit Agnostic Destinations
Cuong Ngoc Tran cuongtran@mnm-team.org
Vitalian Danciu danciu@mnm-team.org

## Slide 2: Large-scale distribution of content
Unicast:
Inefficient use of
transmission resource/channel
Multicast:
Complicated management
Usage initiation requires management intervention
Sender
Receiving
End-points
Sender
Receiving
End-points
Routers
Routers
Join/leave
Notes: Revise the animation of the packet.

## Slide 3: Knowledge distribution and group management
Notes: require network management to authorize a service session
require the user to execute a network management action
transfer knowledge of group membership on the application level to a multicast group
introduce state to the otherwise state-less IP communication
limited deployment, ALM is prefered
ALM:
Multicast function is moved to application layer
Require receiver-side configuration
Does not profit from network support
Xcast:
multicast with explicit unicast addresses
efficient data delivery with network support
gradual deployment by using ALM but with high-latency data delivery
Support max. 64 participants

## Slide 4: Approach
https://www.lifehack.org/articles/lifestyle/10-the-best-mead-recipes.html

## Slide 5: Approach
Multicast to Explicit Agnostic Destinations (MEADcast)
“Slow start” of multiple unicast
Discover network support
Consolidate unicast stream into MEADcast where possible
All knowledge + management are at sender side, none at receiver
Notes: One-to-many communication
Group management at sender
Agnostic receiving end-point
Stateless data delivery at router
Privacy amongst receiving end-points
Efficient data delivery with support from network, otherwise unicast
Support for gradual deployment
Support a large number of participants

## Slide 6: MEADcast functions
Topology discovery
  Sender discovers MEADcast-aware routers (MEADcast router) on all paths towards receiving end-points
Data delivery
  Sender transmits data based on the discovered topology
Notes: R 0 does not drop the message since the option type identifier of MEADcast header is 00 [10].

## Slide 7: MEADcast header
S |E1
R1 | E1 | E2 | R2 | E3 | E4
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
IPv6 header
MEADcast header
(IPv6 extension header)
Address list
Router-map
Bitmap
Address list : contains IPv6 addresses of receivers and delivering routers
Router-map : marks the position of routers in the address list (bit = 1)
Bitmap : marks if a router still waits for MEADcast message (bit = 1)

## Slide 8: Data delivery : All MEADcast network
S |E1
S |E2
S |E3
S |E4
IPv6 header
MEADcast header
(IPv6 extension header)
S |E1
R1 |E1|E2|R2|E3|E4
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
Sender’s viewpoint
S |E1
R1 |E1|E2
1 | 0 | 0
1 | 0 | 0
S |E3
R2 |E3|E4
1 | 0 | 0
1 | 0 | 0

## Slide 9: Topology Discovery: All MEADcast network
1. Sender sends
discovery requests
2. MEADcast Router:
+ sends discovery response,
+ forwards discovery request
3. Receiver drops
discovery request
4. Sender composes
topology based on
discovery responses
MEADcast Router

## Slide 10: Topology Discovery: All MEADcast network
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 1, E1
Disc. Req
# hop = 1, E2
Disc. Req
# hop = 1, E3
Disc. Req
# hop = 1, E4
Disc. Req
# hop = 2, E2
Disc. Req
# hop = 2, E3
Disc. Req
# hop = 2, E1
Disc. Req
# hop = 2, E4
Disc. Resp
# hop = 1, E3, R0
Disc. Resp
# hop = 1, E4, R0
Disc. Resp
# hop = 1, E1, R0
Disc. Resp
# hop = 1, E2, R0
Disc. Resp
# hop = 2, E1, R1
Disc. Resp
# hop = 2, E2, R1
Disc. Resp
# hop = 2, E3, R2
Disc. Resp
# hop = 2, E4, R2

## Slide 11: Topology Discovery: Sparse MEADcast network
1. Sender sends
discovery requests
2. MEADcast Router:
+ sends discovery response,
+ forwards discovery request
3. Receiver drops
discovery request
4. Sender composes
topology based on
discovery responses
MEADcast Router
Normal Router

## Slide 12
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 1, E3
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 1, E4
Disc. Resp
# hop = 1, E3, R2
Disc. Resp
# hop = 1, E4, R2

## Slide 13: Data delivery: Sparse MEADcast network
S |E1
S |E2
S |E3
S |E4
S |E1
S |E2
IPv6 header
MEADcast header
(IPv6 extension header)
S |E3
R2|E3|E4
1 | 0 | 0
1 | 0 | 0
Sender’s viewpoint

## Slide 14: Relation to upper layers
Sender TCP/IP stack needs to be changed:
App
Transport
Network
…
Application sends
group spec + add + delete
App
UDP
MEADcast
IP
…

## Slide 15: Overhead and Gain
The number of addresses in MEADcast header: 8, 16, 32, 64
Payload size
Maximum transmission unit
Overhead and fragmentation
IP HEADER
MEADcast extension HEADER
Payload
fixed
variable
variable
MTU (fixed)
Trade-off: multiplicity vs payload size

## Slide 16: Study of efficiency

## Slide 17: Traffic saving (vs. Unicast)

## Slide 18: Result
Total data volume in the whole network when sender transmits 800 MB data
40%
62%
77%
81%
% traffic saving

## Slide 19: Take-away
One-to-many communication
Group management at sender
Agnostic receiving end-point
Efficient data delivery with support from network, otherwise unicast
Stateless data delivery by MEADcast router
Support for gradual deployment
Support a large number of participants
MEADcast
cuongtran@mnm-team.org
danciu@mnm-team.org

## Slide 20: Backup slides

## Slide 21: Experiment setup
Number of addresses in MEADcast header: 8, 16, 32, 64
Percentage of MEADcast routers in the topology: 0, 10%, 30%, 50%, 70%, 100%
Number of receivers: 100, 200, 300 … 900, 1000
Topology: design, random, mix
Service data unit size (payload from the application layer): 500, 600, 700, 800, 900 … 1500

## Slide 22: Fragmentation by payload

## Slide 23: Fragmentation by # receivers

## Slide 24: Evaluation
Total traffic volume in the whole network [mb] when sender transmits 800 MB data
(* indicates designed topology.)

## Slide 25: Application Layer Multicast
Multicast function is moved to application layer
Require receiver-side configuration
Does not profit from network support
Some receivers maintain the other receivers’ identity  privacy issue
Sender
Receivers
Routers

## Slide 26: Xcast (rfc5058)
multicast with explicit unicast addresses
efficient data delivery with network support
gradual deployment by using ALM but with high-latency data delivery
Support max. 64 participants
In gradual deployment, each receiver see the other receivers’ identity  privacy issue
Sender
Receivers
Routers
Notes: support a very large number of small multicast sessions (each < 64 participants)

## Slide 27: Compare to Multicast
TODO:
Show a scenario for multicast data delivery, similar to that of MEADcast. Point out what the sender, router and receivers have to do.
Compare to MEADcast

## Slide 28: MEADcast header
Use bitmap and router-map to mark position of router in the MEADcast address list
A router whose address is in MEADcast header is responsible for all its continuous subsequent end-point addresses

## Slide 29: Topology discovery
Sender rules for composing discovery:
Only MEADcast router which is responsible for at least two receiving end-points is put in MEADcast header, otherwise unicast
Farther router (higher hop count from sender) has higher priority to occupy a position in MEADcast header
If one MR sends discovery responses to sender with two different hop-counts, the response with larger hop count is eliminated in building the topology

## Slide 30: Topology Discovery: All MEADcast network
1. Sender sends
discovery requests
2. MEADcast Router:
+ sends discovery response,
+ forwards discovery request
3. Receiver drops
discovery request
4. Sender composes
topology based on
discovery responses
MEADcast Router

## Slide 31: Topology Discovery: All MEADcast network
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 1, E1
Disc. Req
# hop = 1, E2
Disc. Req
# hop = 1, E3
Disc. Req
# hop = 1, E4
Disc. Req
# hop = 2, E2
Disc. Req
# hop = 2, E3
Disc. Req
# hop = 2, E1
Disc. Req
# hop = 2, E4
Disc. Resp
# hop = 1, E1, R0
Disc. Resp
# hop = 1, E2, R0
Disc. Resp
# hop = 1, E3, R0
Disc. Resp
# hop = 1, E4, R0
Disc. Resp
# hop = 2, E1, R1
Disc. Resp
# hop = 2, E2, R1
Disc. Resp
# hop = 2, E3, R2
Disc. Resp
# hop = 2, E4, R2

## Slide 32: Topology Discovery: Sparse MEADcast network
1. Sender sends
discovery requests
2. MEADcast Router:
+ sends discovery response,
+ forwards discovery request
3. Receiver drops
discovery request
4. Sender composes
topology based on
discovery responses
MEADcast Router
Normal Router

## Slide 33
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 0, E3
Disc. Req
# hop = 0, E4
Disc. Req
# hop = 0, E2
Disc. Req
# hop = 1, E3
Disc. Req
# hop = 0, E1
Disc. Req
# hop = 1, E4
Disc. Resp
# hop = 1, E3, R2
Disc. Resp
# hop = 1, E4, R2

## Slide 34
Show a scenario of topology with cycle (loop)

## Slide 35: Example
S |E1
R0 |E1|E2|R2|E3|E4
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
S |E3
R2 |E3|E4
1 | 0 | 0
1 | 0 | 0
S |E1
S |E2
S |E3
S |E4

## Slide 36: Example
S |E1
R1 |E1|E2|E3
1 | 0 | 0 | 0
1 | 0 | 0 | 0
S |E3
S |E1
S |E2

## Slide 37: Example
S |E1
R0 |E1|R2|E2|E3
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0
S |E2
R2 |E2|E3
1 | 0 | 0
1 | 0 | 0
S |E1
S |E2
S |E3

## Slide 38: Example
S |E1
R2|E2|E3
1 | 0 | 0
1 | 0 | 0
S |E2
R2 |E2|E3
1 | 0 | 0
1 | 0 | 0
S |E1
S |E2
S |E3
However, if we don’t want an MEADcast router responsible for only 1 receiver
in MEADcast address list
S |E1

## Slide 39: Example
S |E1
R1 |E1
1 | 0
1 | 0
S |E1
S |E2
S |E3

## Slide 40
S |E1
R1 |E1|E2|E3
1 | 0 | 0 | 0
1 | 0 | 0 | 0
S |E3
S |E1
S |E2